## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 3 Transport Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (April 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on QUIC, CUBIC, delay-based congestion control
lighter header font

## Slide 2: Transport layer: overview
Our goal:
understand principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
learn about Internet transport layer protocols:
  UDP: connectionless transport
  TCP: connection-oriented reliable transport
  TCP congestion control

## Slide 3: Transport layer: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 4: Transport services and protocols
provide logical communication between application processes running on different hosts
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
transport protocols actions in end systems:
  sender: breaks application messages into segments, passes to network layer
  receiver: reassembles segments into messages, passes to application layer
two transport protocols available to Internet applications
  TCP, UDP
Notes: By logical communication , we
mean that from an application’s perspective, it is as if the hosts running the processes
were directly connected; in reality, the hosts may be on opposite sides of the
planet, connected via numerous routers and a wide range of link types. Application
processes use the logical communication provided by the transport layer to send
messages to each other, free from the worry of the details of the physical infrastructure
used to carry these messages.
Let’s look at each of these three (logical communications, actions,

## Slide 5: Transport vs. network layer services and protocols
household analogy:
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service

## Slide 6: Transport vs. network layer services and protocols
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
household analogy:
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service

## Slide 7: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
Sender:
app. msg
is passed an application-layer message
determines segment header fields values
creates segment
passes segment to IP
transport
Th
Th
app. msg

## Slide 8: Transport Layer Actions
physical
link
network (IP)
application
physical
link
network (IP)
application
transport
transport
Receiver:
app. msg
extracts application-layer message
checks header values
receives segment from IP
Th
app. msg
demultiplexes message up to application via socket

## Slide 9: Two principal Internet transport protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  reliable, in-order delivery
  congestion control
  flow control
  connection setup
UDP: User Datagram Protocol
  unreliable, unordered delivery
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees

## Slide 10: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 11
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg

## Slide 12
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg

## Slide 13
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
HTTP msg
Ht
Hn
HTTP msg

## Slide 14
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client
HTTP msg
Ht
Hn

## Slide 15
transport
physical
link
network
transport
application
physical
link
network
transport
application
physical
link
network
HTTP server
client1
client2
P-client1
P-client2

## Slide 16: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:

## Slide 17: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 18: Connectionless demultiplexing
Recall:
when creating socket, must specify host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when receiving host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP/UDP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at receiving host

## Slide 19: Connectionless demultiplexing: an example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 20: Connection-oriented demultiplexing
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
server may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
  each socket associated with a different connecting client
demux: receiver uses all four values (4-tuple) to direct segment to appropriate socket

## Slide 21: Connection-oriented demultiplexing: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
server: IP address B
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets

## Slide 22: Summary
Multiplexing, demultiplexing: based on segment, datagram header field values
UDP: demultiplexing using destination port number (only)
TCP: demultiplexing using 4-tuple: source and destination IP addresses, and port numbers
Multiplexing/demultiplexing happen at all layers

## Slide 23: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 24: UDP: User Datagram Protocol
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
no connection establishment (which can add RTT delay)
simple: no connection state at sender, receiver
small header size
no congestion control
  UDP can blast away as fast as desired!
  can function in the face of congestion
Why is there a UDP?
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others

## Slide 25: UDP: User Datagram Protocol
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
  HTTP/3
if reliable transfer needed over UDP (e.g., HTTP/3):
  add needed reliability at application layer
  add congestion control at application layer

## Slide 26: UDP: User Datagram Protocol [RFC 768]
Notes: read this RFC – it’s only 2.5 pages!

## Slide 27: UDP: Transport Layer Actions
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application

## Slide 28: UDP: Transport Layer Actions
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP sender actions:
SNMP msg
is passed an application-layer message
determines UDP segment header fields values
creates UDP segment
passes segment to IP
UDPh
UDPh
SNMP msg

## Slide 29: UDP: Transport Layer Actions
SNMP server
SNMP client
transport
(UDP)
physical
link
network (IP)
application
transport
(UDP)
physical
link
network (IP)
application
UDP receiver actions:
SNMP msg
extracts application-layer message
checks UDP checksum header value
receives segment from IP
UDPh
SNMP msg
demultiplexes message up to application via socket

## Slide 30: UDP segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
data to/from application layer

## Slide 31: UDP checksum
Transmitted: 5 6 11
Goal: detect errors (i.e., flipped bits) in transmitted segment
Received: 4 6 11
1st number
2nd number
sum
receiver-computed
checksum
sender-computed
checksum (as received)
=

## Slide 32: UDP checksum
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  Not equal - error detected
  Equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 33: Internet checksum: an example
example: add two 16-bit integers
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1

## Slide 34: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 35: Summary: UDP
“no frills” protocol:
  segments may be lost, delivered out of order
  best effort service: “send and hope for the best”
UDP has its plusses:
  no setup/handshaking needed (no RTT incurred)
  can function when network service is compromised
  helps with reliability (checksum)
build additional functionality on top of UDP in application layer (e.g., HTTP/3)

## Slide 36: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 37: Principles of reliable data transfer
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: note arrows through reliable data transfer channel is just one way – reliably send from sender to receiver

## Slide 38: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
sending process
data
receiving process
data
reliable channel
application
transport
reliable service abstraction
Notes: Spend some time talking about how its to the sender and receiver side protocol that IMPLEMENTS reliable data transfer
Communication over unreliable channel is TWO-way: sender and receiver will exchange messages back and forth to IMPLEMENT one-way reliable data transfer

## Slide 39: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Complexity of reliable data transfer protocol will depend (strongly) on characteristics of unreliable channel (lose, corrupt, reorder data?)
Notes: So we have a sender side and a receiver side. How much work they’ll have to do depends on the IMPAIRMENTS introduced by channel – if the channel is perfect – no problem!

## Slide 40: Principles of reliable data transfer
sending process
data
receiving process
data
application
transport
reliable service implementation
unreliable channel
network
transport
sender-side of
reliable data transfer protocol
receiver-side
of reliable data transfer protocol
Sender, receiver do not know the “state” of each other, e.g., was a message received?
unless communicated via a message
Notes: Here’s a point of view to keep in mind – it’s easy for US to look at sender and receiver together and see what is happening. OH – that message sent was lost.
But think about it say from senders POV How does the sender know if its transmitted message over the unreliable channel got though?? ONLY if receiver somehow signals to the sender that it was received.
The key point here is that one side does NOT know what is going on at the other side – it’s as if there’s a curtain between them. Everything they know about the other can ONLY be learned by sending/receiving messages.
Sender process wants to make sure a segment got through. But it can just somehow magically look through curtain to see if receiver got it. It will be up to the receiver to let the sender KNOW that it (the receiver) has correctly received the segment.
How will the sender and receiver do that – that’s the PROTOCOL.
Before starting to develop a protocol, let’s look more closely at the interface (the API if you will)

## Slide 41: Reliable data transfer protocol (rdt): interfaces
sending process
data
receiving process
data
unreliable channel
sender-side
implementation of rdt reliable data transfer protocol
receiver-side
implementation of rdt reliable data transfer protocol
rdt_send()
udt_send()
rdt_rcv()
deliver_data()
data
Header
data
Header
rdt_send(): called from above, (e.g., by app.). Passed data to deliver to receiver upper layer
udt_send(): called by rdt
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on receiver side of channel
deliver_data(): called by rdt to deliver data to upper layer
Bi-directional communication over unreliable channel
data
packet

## Slide 42: Reliable data transfer: getting started
We will:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow in both directions!
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions
use finite state machines (FSM) to specify sender, receiver
Notes: SO let’s get started in developing our reliable data transfer protocol, which we’ll call rdt (need a good acronym for protocol – like HTTP, TCP, UDP, IP)
Bullet points 1 and 2
NOW if we are going to develop a protocol, so we’ll need some way to SPECIFY a protocol. How do we do that?
We could write text, but as all know, that’s prone to misinterpretation, and might be incomplete. You might write a specification, and then think “oh yeah – I forgot about that case”
What we need is more formal way to specify a protocol. In fact, with a formal specification there may be ways to PROVE PROPERTIES about a specification. But that’s an advanced topic we won’t get into here. We’ll start here by adopting a fairly simple protocol specification technique known as finite state machines (FSM)
And as the name might suggest, a central notion of finite state machines is the notion of STATE
<talk about state>

## Slide 43: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
rdt_rcv(packet)
Wait for call from below
receiver
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
sender
Wait for call from above
Notes: We’ll start with the simplest case possible - an unreliable channel that is, in fact perfect – no segments are lost, corrupted, dupplicated or reordered. The sender just sends and it pops out the other side(perhaps after some delay) perfectly.

## Slide 44: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors?
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
stop and wait
sender sends one packet, then waits for receiver response

## Slide 45: rdt2.0: FSM specifications
Wait for call from above
udt_send(sndpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)

## Slide 46: rdt2.0: FSM specification
Wait for call from above
udt_send(sndpkt)
Wait for ACK or NAK
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
Wait for call from below
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver
Note: “state” of receiver (did the receiver get my message correctly?) isn’t known to sender unless somehow communicated from receiver to sender
that’s why we need a protocol!
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
isNAK(rcvpkt)
isACK(rcvpkt)

## Slide 47: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
udt_send(sndpkt)
udt_send(NAK)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
sender
receiver
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)

## Slide 48: rdt2.0: corrupted packet scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
udt_send(NAK)
rdt_rcv(rcvpkt) && corrupt(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
L
sender
receiver

## Slide 49: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet, then waits for receiver response

## Slide 50: rdt2.1: sender, handling garbled ACK/NAKs
Wait for call 0 from above
Wait for ACK or NAK 0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt)
&& (corrupt(rcvpkt) ||
isNAK(rcvpkt) )
Wait for
call 1 from above
Wait for ACK or NAK 1
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
L
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt) && isACK(rcvpkt)
L

## Slide 51: rdt2.1: receiver, handling garbled ACK/NAKs
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 52: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 53: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt
As we will see, TCP uses this approach to be NAK-free

## Slide 54: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 55: rdt3.0: channels with errors and loss
New channel assumption: underlying channel can also lose packets (data, ACKs)
  checksum, sequence #s, ACKs, retransmissions will be of help … but not quite enough
Q: How do humans handle lost sender-to-receiver words in conversation?

## Slide 56: rdt3.0: channels with errors and loss
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
    retransmission will be duplicate, but seq #s already handles this!
    receiver must specify seq # of packet being ACKed
timeout
use countdown timer to interrupt after “reasonable” amount of time

## Slide 57: rdt3.0 sender
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
Wait for
call 0 from above
Wait for ACK1
Notes: We see the familiar four state sender from our rdt 2.1 and 2.2 protocols. Top two states when sending packet with zero seq # and bottom two

## Slide 58: rdt3.0 sender
Wait for ACK0
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
stop_timer
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
udt_send(sndpkt)
start_timer
timeout
Wait for
call 0 from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
L
rdt_rcv(rcvpkt)
L
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
L
Notes: We see the familiar four state sender from our rdt 2.1 and 2.2 protocols. Top two states when sending packet with zero seq # and bottom two

## Slide 59: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 60: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
ack1
send ack1
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
pkt1
(ignore)
rcv ack1

## Slide 61: Performance of rdt3.0 (stop-and-wait)
example: 1 Gbps link, 15 ms prop. delay, 8000 bit packet
  U sender: utilization – fraction of time sender busy sending
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
  time to transmit packet into channel:
Notes: if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources
Let’s develop a formula for utilization

## Slide 62: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 63: rdt3.0: stop-and-wait operation
sender
receiver
Usender
=
L / R
RTT
RTT
L/R
+ L / R
=
0.00027
=
.008
30.008
rdt 3.0 protocol performance stinks!
Protocol limits performance of underlying infrastructure (channel)

## Slide 64: rdt3.0: pipelined protocols operation
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged packets
  range of sequence numbers must be increased
  buffering at sender and/or receiver

## Slide 65: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!
Notes: two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 66: Go-Back-N: sender
sender: “window” of up to N, consecutive transmitted but unACKed pkts
  k-bit seq # in pkt header
cumulative ACK: ACK(n): ACKs all packets up to, including seq # n
  on receiving ACK(n): move window forward to begin at n+1
timer for oldest in-flight packet
timeout(n): retransmit packet n and all higher seq # packets in window
Notes: window size of 14, 8 have been sent but are not yet ackowledgedm 6 sequence numbers are available for us. In woindow, but no calls from above to use them.
Note – we’ll skip the Go-Back-N FSM specification you can chack that out in powerpoitn slides or book)
TCP uses cumulative ACK

## Slide 67: Go-Back-N: receiver
ACK-only: always send ACK for correctly-received packet so far, with highest in-order seq #
  may generate duplicate ACKs
  need only remember rcv_base
on receipt of out-of-order packet:
  can discard (don’t buffer) or buffer: an implementation decision
  re-ACK pkt with highest in-order seq #
rcv_base
received and ACKed
Out-of-order: received but not ACKed
Not received
Receiver view of sequence number space:
…
…
Notes: Note – we’ll skip the Go-Back-N FSM specification (actually it’s

## Slide 68: Go-Back-N in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
pkt 2 timeout
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
Notes: Let’s skip FSM specification for GBN – check out the book or ppt – and let’s watch GBN sender and receivers in action.
Let assume a window size of 4. at t=0, sender sends packets 0, 1, 2 3, 4, and packet 2 will be lost
At the receiver:
Packet 0 received ACK0 generated
Packet 1 received ACK1 generated
Packet 2 is lost, and so when packet 3 is received, ACK 1 is sent – that’s the cumulative ACK, re-Acknowledging the receipt of packet 1. and in this implementation packet 3 is discarded

## Slide 69: Selective repeat
receiver individually acknowledges all correctly received packets
  buffers packets, as needed, for eventual in-order delivery to upper layer
sender times-out/retransmits individually for unACKed packets
  sender maintains timer for each unACKed pkt
sender window
  N consecutive seq #s
  limits seq #s of sent, unACKed packets
Notes: An important mechanism of GBN was the use of the cumulative acknowledgements, and as we mentioned, cumulative ACKs are used in TCP
An alternate ACK mechanism would be for the receiver to indiviually acknowledge specific packets as they are received. This mechanism is at the heart of the Selective repeat protocol.

## Slide 70: Selective repeat: sender, receiver windows

## Slide 71: Selective repeat: sender and receiver
data from above:
if next available seq # in window, send packet
timeout(n):
resend packet n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark packet n as received
if n smallest unACKed packet, advance window base to next unACKed seq #
sender
packet n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order packets), advance window to next not-yet-received packet
packet n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver
Notes: If the packet is in order, its data will be delivered, as will any buffered data that can now be delived in order

## Slide 72: Selective Repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
send pkt2
(but not 3,4,5)
X
loss
pkt 2 timeout
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack0, send pkt4
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
rcv ack1, send pkt5
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
record ack3 arrived
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
Q: what happens when ack2 arrives?

## Slide 73: Selective repeat: a dilemma!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3

## Slide 74: Selective repeat: a dilemma!
Q: what relationship is needed between sequence # size and window size to avoid problem in scenario (b)?
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
example:
seq #s: 0, 1, 2, 3 (base 4 counting)
window size=3
receiver can’t see sender side
receiver behavior identical in both cases!
something’s (very) wrong!

## Slide 75: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 76: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Typical MSS is 1460 bytes

## Slide 77: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification

## Slide 78: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor

## Slide 79: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-toB segment that triggered that ACK
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK

## Slide 80: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 81: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: This is how TCP re-computes the estimated RTT each time a new SampleRTT is taken.
The process is knows as an exponeitally weighted moving average, shown by the equation here.
<say it>
Where alpha reflects the influence of the most recent measurements on the estimated RTT; a typical value of alpha used in implementaitons is .125
The graph at the bottom show measured RTTs beween a host in the Massachusetts and a host in France, as well as the estimated, “smoothed” RTT

## Slide 82: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT: want a larger safety margin
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
DevRTT = (1-)*DevRTT + *|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
DevRTT: EWMA of SampleRTT deviation from EstimatedRTT:
Notes: Given this value of the estimated RTT, TCP computes the timeout interval to be the estimated RTT plus a “safety margin”
And the intuition is that if we are seeing a large variation in SAMPLERTT – the RTT estimates are fluctuating a lot - then we’ll want a larger savety margin
So TCP computes the Timeout interval to be the Estimated RTT plus 4 times a measure of deviation in the RTT.
The deviation in the RTT is computed as the eWMA of the difference between the most recently measured SampleRTT from the Estimated RTT

## Slide 83: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: Given these details of TCP sequence numbers, acks, and timers, we can now describe the big picture view of how the TCP sender and receiver operate
You can check out FSMs in book; let’s just give an English text description here and let’s start with the sender.

## Slide 84: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: Rather than immediately ACKnowledig this segment, many TCP implementations will wait for half a second for another in-order segment to arrive, and then generate a single cumulative ACK for both segments – thus decreasing the amount of ACK traffic. The arrival of this second in-order segment and the cumulative ACK generation that covers both segments is the second row in this table.

## Slide 85: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: To cement our understanding of TCP reliability, let’s look a a few retransmission scenarios
In the first case a TCP segments is transmited and the ACK is lost, and the TCP timeout mechanism results in another copy of being transmitted and then re-ACKed a the sender
In the second example two segments are sent and acknowledged, but there is a premature timeout e for the first segment, which is retransmitted. Notet that when this retransmitted segment is received, the receiver has already received the first two segments, and so resends a cumulative ACK for both segments received so far, rather than an ACK for just this fist segment.

## Slide 86: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: And in this last example, two segments are again transmitted, the first ACK is lost but the second ACK, a cumulative ACK arrives at the sender, which then can transmit a third segment, knowing that the first two have arrived, even though the ACK for the first segment was lost

## Slide 87: TCP fast retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: Let’s wrap up our study of TCP reliability by discussing an optimization to the original TCP known as TCP fast retransmit,
Take a look at this example on the right where 5 segments are transmitted and the second segment is lost. In this case the TCP receiver sends an ACK 100 acknowledging the first received segment.
When the third segment arrives at the receiver, the TCP receiver sends another ACK 100 since the second segment has not arrived. And similarly for the 4th and 5th segments to arrive.
Now what does the sender see? The sender receives the first ACK 100 it has been hoping for, but then three additional duplicate ACK100s arrive. The sender knows that somethings’ wrong – it knows the first segment arrived at the receiver but three later arriving segments at the receiver – the ones that generated the three duplicate ACKs – we received correctly but were not in order. That is, that there was a missing segment at the receiver when each of the three duplicate ACK were generated.
With fast retransmit, the arrival of three duplicate ACK causes the sender to retransmit its oldest unACKed segment, without waiting for a timeout event. This allows TCP to recover more quickly from what is very likely a loss event
specifically that the second segment has been lost, since three higher -numbered segments were received

## Slide 88: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 89: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers
Notes: (Presuming an intro)
Before diving into the details of TCP flow control, let’s first get the general context and motivate the need for flow control.
This diagram show a typical transport-layer implementation
A segment is brought up the protocol stack to the transport layer, and the segment’s payload is removed from the segment and written INTO socket buffers.
How does data get taken OUT of socket buffers? By applications performing socket reads, as we learned in Chapter 2.
And so the question is “What happens if network layer delivers data faster than an application-layer process removes data from socket buffers?”
Let’s watch a video of what happens when things arrive way too fast to fast to be processed.
<video>. (I love that video). Another human analogy showing the need for flow control is the saying – to use some English slang - “no one can drink from a firehose”
Flow control is a mechanism to the calamity of a receiver being over-run by a sender that is sending too fast – it allows the RECEIVER to explictly control the SENDER so sender won’t overflow receiver’s buffer by transmitting too much, too fast

## Slide 90: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
from sender
Application removing data from TCP socket buffers
receive window
flow control: # bytes receiver willing to accept
Notes: (Presuming an intro)
Before diving into the details of TCP flow control, let’s first get the general context and motivate the need for flow control.
This diagram show a typical transport-layer implementation
A segment is brought up the protocol stack to the transport layer, and the segment’s payload is removed from the segment and written INTO socket buffers.
How does data get taken OUT of socket buffers? By applications performing socket reads, as we learned in Chapter 2.
And so the question is “What happens if network layer delivers data faster than an application-layer process removes data from socket buffers?”
Let’s watch a video of what happens when things arrive way too fast to fast to be processed.
<video>. (I love that video). Another human analogy showing the need for flow control is the saying – to use some English slang - “no one can drink from a firehose”
Flow control is a mechanism to the calamity of a receiver being over-run by a sender that is sending too fast – it allows the RECEIVER to explictly control the SENDER so sender won’t overflow receiver’s buffer by transmitting too much, too fast

## Slide 91: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control
from sender
Application removing data from TCP socket buffers
Notes: (Presuming an intro)
Before diving into the details of TCP flow control, let’s first get the general context and motivate the need for flow control.
This diagram show a typical transport-layer implementation
A segment is brought up the protocol stack to the transport layer, and the segment’s payload is removed from the segment and written INTO socket buffers.
How does data get taken OUT of socket buffers? By applications performing socket reads, as we learned in Chapter 2.
And so the question is “What happens if network layer delivers data faster than an application-layer process removes data from socket buffers?”
Let’s watch a video of what happens when things arrive way too fast to fast to be processed.
<video>. (I love that video). Another human analogy showing the need for flow control is the saying – to use some English slang - “no one can drink from a firehose”
Flow control is a mechanism to the calamity of a receiver being over-run by a sender that is sending too fast – it allows the RECEIVER to explictly control the SENDER so sender won’t overflow receiver’s buffer by transmitting too much, too fast

## Slide 92: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP receiver-side buffering
Notes: Here’s how TCP implement flow control. The basic idea is simple – the receiver informs the sender how much free buffer space there is, and the sender is limited to send no more than this amount of data. That the value o RWND in the diagram to the right.
This information is carried from the receiver to the sender in the “receiver advertised window” (do a PIP of header) in the TCP header, and the value will change as the amount of free buffer space fluctuates over time.

## Slide 93: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
flow control: # bytes receiver willing to accept
receive window
TCP segment format
Notes: Here’s how TCP implement flow control. The basic idea is simple – the receiver informs the sender how much free buffer space there is, and the sender is limited to send no more than this amount of data. That the value o RWND in the diagram to the right.
This information is carried from the receiver to the sender in the “receiver advertised window” (do a PIP of header) in the TCP header, and the value will change as the amount of free buffer space fluctuates over time.

## Slide 94: TCP connection management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: The other TCP topic we’ll want to consider here is that of “connection management”
The TCP sender and reciver have a number of pieces of shared state that they must establish before actually communication
FIRST theym ust both agree that they WANT to communicate with each other
Secondly there are connection parameters – the initial sequence number and the initial receiver-advertised bufferspace that they’ll want to agree on
This is done via a so-called handshake protocol – the client reaching our to the server, and the server answering back.
And before diving into the TCP handshake protocol, let’s first consider the problem of handshaking, of establishing shared state.

## Slide 95: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: Here’s an example of a two way handshake. Alice reaches out to Bob and say’s “let’s talk” and Bob says OK, and they start their conversation
For a network protocol, the equivalent protocol would be a client sending a “request connection” message saying ”let’s talk, the initial sequence number is x”
And the server would respond with a message ”I accept your connect x”
And the question we want to ask ourselves is <talk through>
Will this work? Let’s look at a few scenarios…

## Slide 96: 2-way handshake scenarios
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
ACK(x+1)
No problem!

## Slide 97: 2-way handshake scenarios
ESTAB
retransmit
req_conn(x)
req_conn(x)
client terminates
server
forgets x
connection
x completes
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
acc_conn(x)
Problem: half open connection! (no client)

## Slide 98: 2-way handshake scenarios
client terminates
ESTAB
choose x
req_conn(x)
ESTAB
acc_conn(x)
data(x+1)
accept
data(x+1)
connection
x completes
server
forgets x
Problem: dup data
accepted!
data(x+1)
retransmit
data(x+1)
accept
data(x+1)
retransmit
req_conn(x)
ESTAB
req_conn(x)

## Slide 99: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
LISTEN
Server state
LISTEN
clientSocket = socket(AF_INET, SOCK_STREAM)
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
connectionSocket, addr = serverSocket.accept()
clientSocket.connect((serverName,serverPort))
Notes: TCP’s three way handshake, that operates as follows
Let’s say the client and server both create a TCP socket as we learned about in Chapter 2 and enter the LISTEN state
The client then connects to the server sending a SYN message with a sequence number x (SYN Message is an TCP Segment with SYN but set in the header – you might want to go back and review the TCP segment format!)
The server is waiting for a connection, and receives the SYN message enters the SYN received state (NOT the established state and sends a SYN ACK message back.
Finally the client sends an ACK message to the server, and when the server receiver this enters the ESTABLished state. This is when the application process would see the return from the wait on the socket accept() call

## Slide 100: A human 3-way handshake protocol
1. On belay?
2. Belay on.
3. Climbing.
Notes: As usual, there’s a human protocol analogy to the three way handshake, and I still remember thinking about this clinging for my life while climbing up a rockface
When you want start climbing you first say ON BELOW (meaning ARE YOU READY WITH MY SAFETY ROPE)
THE BELYER (server) responds BELAY ON (that lets you know the belayer is ready for you)
And then you say CLIMING
It’s amazing what can pass through your head when your clinging for your life o a

## Slide 101: Closing a TCP connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled
Notes: All good things must come to an end, and that’s true for a TCP connection as well.
And of course there’s a protocol for one side to gracefully close of a TCP connection using a FIN message, to which the other side sends a FINACK message and waits around a bit to respond to any retransmitted FIN messages before timing out.

## Slide 102: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 103: Principles of congestion control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  long delays (queueing in router buffers)
  packet loss (buffer overflow at routers)
different from flow control!
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver
a top-10 problem!

## Slide 104: Causes/costs of congestion: scenario 1
Simplest scenario:
maximum per-connection throughput: R/2
Host A
Host B
throughput: lout
large delays as arrival rate lin approaches capacity
Q: What happens as arrival rate lin approaches R/2?
original data: lin
R
two flows
one router, infinite buffers
input, output link capacity: R
infinite shared output link buffers
R
no retransmissions needed
R/2
delay
lin
R/2
R/2
R/2
lout
lin
throughput:

## Slide 105: Causes/costs of congestion: scenario 2
one router, finite buffers
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
sender retransmits lost, timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : l’in lin
lout
R
R

## Slide 106: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
copy
free buffer space!
Idealization: perfect knowledge
sender sends only when router buffers available
lout
R
R
R/2
lin
R/2
lout
throughput:

## Slide 107: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
no buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost

## Slide 108: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
free buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
when sending at R/2, some packets are needed retransmissions
lin
R/2
lout
throughput:
R/2
“wasted” capacity due to retransmissions

## Slide 109: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
timeout
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
free buffer space!
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 110: Causes/costs of congestion: scenario 2
“costs” of congestion:
more work (retransmission) for given receiver throughput
unneeded retransmissions: link carries multiple copies of a packet
  decreasing maximum achievable throughput
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 111: Causes/costs of congestion: scenario 3
four senders
multi-hop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data

## Slide 112: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any upstream transmission capacity and buffering used for that packet was wasted!
R/2
R/2
lout
lin’

## Slide 113: Causes/costs of congestion: insights
upstream transmission capacity / buffering wasted for packets lost downstream
delay increases as capacity approached
un-needed duplicates further decreases effective throughput
loss/retransmission decreases effective throughput
throughput can never exceed capacity

## Slide 114: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP

## Slide 115: Approaches towards congestion control
TCP ECN, ATM, DECbit protocols
data
data
ACKs
ACKs
explicit congestion info
Network-assisted congestion control:
routers provide direct feedback to sending/receiving hosts with flows passing through congested router
may indicate congestion level or explicitly set sending rate

## Slide 116: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 117: TCP congestion control: AIMD
approach: senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
time
  increase sending rate by 1 maximum segment size every RTT until loss detected
Additive Increase
  cut sending rate in half at each loss event
Multiplicative Decrease

## Slide 118: TCP AIMD: more
Multiplicative decrease detail: sending rate is
Cut in half on loss detected by triple duplicate ACK (TCP Reno)
Cut to 1 MSS (maximum segment size) when loss detected by timeout (TCP Tahoe)
Why AIMD?
AIMD – a distributed, asynchronous algorithm – has been shown to:
  optimize congested flow rates network wide!
  have desirable stability properties

## Slide 119: TCP congestion control: details
TCP sender limits transmission:
cwnd is dynamically adjusted in response to observed network congestion (implementing TCP congestion control)
LastByteSent- LastByteAcked
<
cwnd
last byte
ACKed
last byte sent
cwnd
sender sequence number space
available but not used
TCP sending behavior:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
TCP rate
~
~
cwnd
RTT
bytes/sec
sent, but not-yet ACKed
(“in-flight”)

## Slide 120: TCP slow start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
summary: initial rate is slow, but ramps up exponentially fast

## Slide 121: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
X

## Slide 122: Summary: TCP congestion control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!

## Slide 123: TCP CUBIC
Is there a better way than AIMD to “probe” for usable bandwidth?
Wmax
Wmax/2
classic TCP
TCP CUBIC - higher throughput in this example
Insight/intuition:
  Wmax: sending rate at which congestion loss was detected
  congestion state of bottleneck link probably (?) hasn’t changed much
  after cutting rate/window in half on loss, initially ramp to to Wmax faster, but then approach Wmax more slowly

## Slide 124: TCP CUBIC
K: point in time when TCP window size will reach Wmax
  K itself is tuneable
  larger increases when further away from K
  smaller increases (cautious) when nearer K
TCP
sending
rate
time
TCP Reno
TCP CUBIC
Wmax
t0
t1
t2
t3
t4
TCP CUBIC default in Linux, most popular TCP for popular Web servers
increase W as a function of the cube of the distance between current time and K

## Slide 125: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
bottleneck link (almost always busy)
packet queue almost never empty, sometimes overflows packet (loss)

## Slide 126: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
understanding congestion: useful to focus on congested bottleneck link
insight: increasing TCP sending rate will not increase end-end throughout with congested bottleneck
insight: increasing TCP sending rate will increase measured RTT
RTT
Goal: “keep the end-end pipe just full, but not fuller”

## Slide 127: Delay-based TCP congestion control
Keeping sender-to-receiver pipe “just full enough, but no fuller”: keep bottleneck link busy transmitting, but avoid high delays/buffering
RTTmeasured
Delay-based approach:
RTTmin - minimum observed RTT (uncongested path)
uncongested throughput with congestion window cwnd is cwnd/RTTmin
if measured throughput “very close” to uncongested throughput
increase cwnd linearly /* since path not congested */
else if measured throughput “far below” uncongested throughout
decrease cwnd linearly /* since path is congested */
RTTmeasured
measured
throughput
=
# bytes sent in last RTT interval

## Slide 128: Delay-based TCP congestion control
congestion control without inducing/forcing loss
maximizing throughout (“keeping the just pipe full… ”) while keeping delay low (“…but not fuller”)
a number of deployed TCPs take a delay-based approach
  BBR deployed on Google’s (internal) backbone network

## Slide 129: Explicit congestion notification (ECN)
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
TCP deployments often implement network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
  policy to determine marking chosen by network operator
congestion indication carried to destination
destination sets ECE bit on ACK segment to notify sender of congestion
involves both IP (IP header ECN bit marking) and TCP (TCP header C,E bit marking)
ECN=10
ECN=11
ECE=1
IP datagram
TCP ACK segment

## Slide 130: TCP fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 131: Q: is TCP Fair?
Example: two competing TCP sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
A: Yes, under idealized assumptions:
same RTT
fixed number of sessions only in congestion avoidance
Is TCP fair?

## Slide 132: Fairness: must all network apps be “fair”?
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
there is no “Internet police” policing use of congestion control
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this , e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 133: Transport layer: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 134: Evolving transport-layer functionality
TCP, UDP: principal transport protocols for 40 years
different “flavors” of TCP developed, for specific scenarios:
moving transport–layer functions to application layer, on top of UDP
  HTTP/3: QUIC
Scenario | Challenges
Long, fat pipes (large data transfers) | Many packets “in flight”; loss shuts down pipeline
Wireless networks | Loss due to noisy wireless links, mobility; TCP treat this as congestion loss
Long-delay links | Extremely long RTTs
Data center networks | Latency sensitive
Background traffic flows | Low priority, “background” TCP flows

## Slide 135: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/2 over QUIC over UDP

## Slide 136: QUIC: Quick UDP Internet Connections
adopts approaches we’ve studied in this chapter for connection establishment, error control, congestion control
multiple application-level “streams” multiplexed over single QUIC connection
  separate reliable data transfer, security
  common congestion control
  error and congestion control: “Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
  connection establishment: reliability, congestion control, authentication, encryption, state established in one RTT

## Slide 137: QUIC: Connection establishment
TCP handshake
(transport layer)
TLS handshake
(security)
TCP (reliability, congestion control state) + TLS (authentication, crypto state)
2 serial handshakes
data
QUIC handshake
data
QUIC: reliability, congestion control, authentication, crypto state
1 handshake

## Slide 138: QUIC: streams: parallelism, no HOL blocking
(a) HTTP 1.1
TLS encryption
TCP RDT
TCP Cong. Contr.
transport
application
(b) HTTP/2 with QUIC: no HOL blocking
TCP RDT
TCP Cong. Contr.
TLS encryption
error!
HTTP
GET
HTTP
GET
HTTP
GET
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
UDP
UDP
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
error!
HTTP
GET
HTTP
GET
HTTP
GET

## Slide 139: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
Up next:
leaving the network “edge” (application, transport layers)
into the network “core”
two network-layer chapters:
  data plane
  control plane

## Slide 140: Additional Chapter 3 slides

## Slide 141: Go-Back-N: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 142: Go-Back-N: receiver extended FSM
Wait
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
udt_send(sndpkt)
any other event
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
ACK-only: always send ACK for correctly-received packet with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order packet:
  discard (don’t buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #

## Slide 143: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above

## Slide 144: TCP 3-way handshake FSM
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket =
newSocket("hostname","port number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L

## Slide 145: Closing a TCP connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB

## Slide 146: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume there is always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec

## Slide 147: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
versions of TCP for long, high-speed scenarios
TCP throughput =
1.22
.
MSS
RTT
L